## Slide 1
English
This presentation is automatically generated.
You can freely edit it and add any extra content you wish.
Español
Esta presentación se genera automáticamente.
Puedes modificarla a tu criterio y añadir cualquier contenido adicional que desees.
Italiano
Questa presentazione è generata automaticamente.
Puoi modificarla liberamente e aggiungere eventuali contenuti extra che desideri.

## Slide 2: The Spirit Level: Is It Straight?
Use your phone's tilt sensor and advanced conditionals ('Else If') to build a tool that tells you if something is perfectly level.

## Slide 3: What will we do?

## Slide 4: More Than Two Options?
You've seen how conditionals can work with two options: IF a condition is true, do something, ELSE do something different. This is perfect for a simple on/off switch.
But what if you need to check for multiple, different conditions?

## Slide 5: Introducing 'Else If'
The “else if” structure lets you chain multiple checks together in a single, neat block. You can think of it like a referee in a soccer match:
IF the foul is very serious, THEN show a red card.
ELSE IF the foul is just a warning, THEN show a yellow card.
ELSE (if neither of the above is true), THEN it’s just a simple foul.
The program checks each condition in order until it finds one that is true.

## Slide 6: ELSE IF: 4 Options for our Spirit Level
We'll use this multi-path logic to program a tilt detector that helps us hang pictures perfectly straight.
The screen will light up with different colors based on the tilt value: green for level, yellow for slightly off, orange for more tilted, and red for very tilted.

## Slide 7: How does the phone detect tilt?
To detect the tilt of a phone, we use a tiny built-in sensor called an accelerometer. This sensor can measure forces like gravity, telling the phone its orientation in space. It measures tilt on three different axes: X (left-right), Y (forward-backward), and Z (up-down). This allows the phone to know if it’s tilted to one side, standing upright, or lying flat.

## Slide 8: Make the Tilt Sensor
Click on Add device and select Inclination.
Click on Add device again and select Lamp.
Add both devices to the same smartphone for this project.
Let’s create a prototype that helps us detect if a picture frame is tilted.

## Slide 9: Code Composition
Click on the question mark icon to open the comments that explain the code.
The "absolute" block (which makes a number positive) is located in the Mathematics category, inside the "square root" block's dropdown menu.
https://app.protobject.com/generate?a15-inclination&en&dynamic&-1

## Slide 10: Reflect
This 'IF / ELSE IF / ELSE' chain is a super powerful tool.
Our spirit level used the Y-axis (forward-backward tilt). What do you think would happen if you changed the code to read the X-axis (left-right tilt) instead?
What other real-world tool or game could you build using your phone's tilt sensor?